## Slide 1
INTERNSHIP PROGRESS REVIEW
EEG-Based Motor Imagery Classification
for BCI Object Control
From a single-subject baseline to a systematic study of what limits cross-subject generalization
Presented by: [Your Name]
Meeting with: [Professor's Name]
Dataset: BCI Competition IV — Dataset 2a
Notes: Good [morning/afternoon]. This is a fuller review than last time — since we last spoke I've expanded well beyond the original pipeline: fixed a real data bug, run a systematic optimization sweep, tried an alternative feature method and a deep learning baseline, and tested two genuinely promising directions — subject adaptation and cross-session evaluation. I'll move quickly through the setup you've already seen and spend most of the time on what's new.

## Slide 2
PROJECT OBJECTIVE
From Imagined Movement to Machine Command
02
Classify motor imagery EEG signals into 4 classes: Left Hand, Right Hand, Foot, Tongue.
Long-term goal: feed the predicted class into a BCI system to control an external object in real time.
This phase: understand why single-subject accuracy (83%) is so much higher than cross-subject accuracy, and find what actually closes that gap.
TODAY'S STORY
Single-subject baseline: 83%
Found & fixed a data bug
Swept CSP / classifier / window
Tried FBCSP & deep learning
Subject adaptation: strongest lead
Cross-session: isolates the real problem
Notes: Quick roadmap: single-subject baseline, a data bug I found and fixed, a systematic sweep of the usual knobs, two alternative methods, and then the two experiments that actually moved the needle — subject adaptation and cross-session evaluation.

## Slide 3
DATASET
BCI Competition IV — Dataset 2a
03
9
Subjects
22
EEG Channels
250 Hz
Sampling Rate
288
Trials / Subject
FOUR MOTOR IMAGERY CLASSES
1
Left Hand
2
Right Hand
3
Foot
4
Tongue
✓ Pooled across all 9 subjects this now totals 2,592 perfectly balanced trials (648 per class) — see Slide 6 for why that number matters.
Notes: Same dataset as before — BCI IV 2a, 9 subjects, 22 channels, 250 Hz, four balanced motor imagery classes. One update: the pooled multi-subject total is now a clean 2,592 trials, which I'll explain in a couple of slides.

## Slide 4
METHODOLOGY
End-to-End Classification Pipeline
04
Raw EEG
GDF load (MNE)
Preprocessing
8-30 Hz band-pass
Epoch Extraction
trial window
Feature Extraction
CSP / FBCSP / EEGNet
Classifier
LDA / SVM
Predicted Class
L / R / Foot / T
EVALUATION PROTOCOLS USED
Single-subject
80/20 split & 5-fold CV within one subject
Multi-subject LOSO
train on 8 subjects, test on the 9th (unseen)
Cross-session
train on a subject's T-session, test their own E-session
Subject adaptation
8 subjects + X% of target, test on target's E-session
Notes: Same core pipeline as before, but the feature-extraction step now branches three ways — CSP, Filter-Bank CSP, and EEGNet — and I use four different evaluation protocols depending on the question: plain single-subject splits, Leave-One-Subject-Out for cross-subject generalization, cross-session for day-to-day variability, and a subject-adaptation protocol that mixes the two.

## Slide 5
RESULTS — BASELINE
Single-Subject Classification (Subject A01)
05
Classifier | CSP Components | Accuracy
LDA (baseline) | 10 | 70.69%
SVM — RBF kernel | 10 (grid-searched) | did not beat linear
SVM — Linear kernel | 12 | 83.0% (5-fold CV)
This remains the project's performance ceiling — the number every cross-subject result is measured against.
83%
Best cross-validated accuracy (chance level = 25%)
CSP COMPONENTS vs. ACCURACY
Chart: CSP components
| 2 | 4 | 6 | 8 | 10 | 12 | 16
Mean CV Accuracy (%) | 74.3 | 79.2 | 78.1 | 80.2 | 82.6 | 83 | 80.5
Notes: Unchanged from before: 83% mean cross-validated accuracy for a single subject, 12 CSP components, linear SVM. This is the ceiling everything else in this deck is measured against.

## Slide 6
DATA INTEGRITY
A Bug I Found, Diagnosed, and Fixed
06
The pooled multi-subject dataset showed an unexplained class imbalance: 648 trials each for Left/Right Hand, but only 576 for Foot/Tongue.
Investigated
Checked A04T's raw file directly — it actually has a perfectly balanced 72 trials per class.
Root Cause
Code assumed a fixed number for each class, but MNE assigns numbers per file — A04T's numbering shifted, so Foot/Tongue got mislabeled as Left/Right.
Fixed
Look up each class by its description string, not a fixed number. Applied to all 4 affected notebooks, then re-ran everything.
2,448 → 2,592
trials (imbalanced → perfectly balanced)
17.4% → 25.0%
A04T's own LOSO accuracy (below chance → at chance)
4 notebooks
patched and re-verified
✓ A04T moving from the worst-performing subject to right at chance level is direct evidence the fix worked — not just a cleaner dataset, a measurably fairer one.
Notes: This is work I'm genuinely proud of. I noticed the pooled dataset had an odd class imbalance, investigated one subject's raw file directly to rule out a data problem, and traced it to a code assumption: I was using a fixed number to identify each class, but MNE actually assigns numbers per file, and one subject's file happened to shift. That subject's real foot and tongue trials were silently getting labeled as left and right hand. I fixed the loading logic in all four affected notebooks and re-ran everything. The cleanest proof it worked: that subject's own held-out accuracy went from below chance to right at chance.

## Slide 7
RESULTS — CORRECTED
Multi-Subject LOSO, On the Fixed Dataset
07
31.40% ± 6.77% — basic LOSO baseline, 16 CSP components, GridSearchCV-tuned RBF-SVM, on the corrected 2,592-trial dataset (up from 28.59% pre-fix).
Subject | Acc. | Subject | Acc. | Subject | Acc.
A01T | 38.5% | A04T | 25.0% | A07T | 31.6%
A02T | 24.7% | A05T | 24.0% | A08T | 37.8%
A03T | 38.9% | A06T | 23.3% | A09T | 38.9%
A04T is no longer the outlier — it now sits in the middle of the pack, right where a chance-level subject should.
CSP COMPONENTS SWEEP (LOSO)
Chart: CSP components
| 4 | 6 | 8 | 12 | 16
Mean LOSO Accuracy (%) | 32.1 | 32.29 | 30.52 | 30.94 | 30.67
Unlike single-subject, more CSP components don't help past 6 — the cross-subject bottleneck isn't feature count.
Notes: With the corrected data, basic LOSO sits at 31.4%, up modestly from the buggy 28.6%. Look at the per-subject table — A04T is no longer the standout worst performer. The CSP sweep shows something different from single-subject too: more components don't keep helping past 6, which tells us the cross-subject ceiling isn't about feature count.

## Slide 8
RESULTS — ABLATION
Optimization Sweep: What Actually Helps
08
Factor Tested | Best Setting | Best Accuracy | Effect Size
CSP components (4/6/8/12/16) | 6 | 32.29% | small
Classifier (LDA / linear / RBF SVM) | LDA | 38.31% | moderate
CSP regularization (none/LW/OAS) | no difference | 38.31% | none
Frequency band (4-40 Hz variants) | 8-30 Hz | 38.31% | small
Epoch time window (0-4s variants) | 0-3 s | 41.44% | largest
One clear pattern: LDA beats SVM here — the opposite of the single-subject case — because on the noisier, pooled cross-subject problem, LDA's simplicity is an advantage. And only the epoch window produced a meaningful gain; regularization and frequency-band tuning made essentially no difference. This tells us the bottleneck isn't signal-processing detail.
Notes: I swept five different knobs independently: CSP components, classifier type, CSP regularization, frequency band, and epoch time window. Only two things mattered at all — switching to LDA over SVM, and shortening the epoch window to 0-3 seconds. Regularization and frequency band tuning did essentially nothing. That's an important negative result: it tells me the ceiling here isn't about signal-processing detail, it's something more fundamental about pooling different people's data.

## Slide 9
RESULTS — ALTERNATIVE METHODS
Beyond CSP: Filter-Bank CSP & Deep Learning
09
CSP + LDA
38.31%
baseline classical method
CSP + 0-3s window + LDA
41.44%
best classical result found
FBCSP + LDA
37.23%
6 sub-bands — underperforms plain CSP
EEGNet (deep learning)
38.81%
comparable to CSP, not better
Neither alternative beats simple CSP + LDA once the epoch window is tuned. EEGNet likely needs more training data than the ~2,300 trials available per fold to show its usual advantage over hand-engineered features — worth revisiting if the dataset grows, but not the priority right now.
Notes: I tried two alternatives to plain CSP: Filter-Bank CSP, which splits the signal into six frequency sub-bands, and EEGNet, a deep learning model built for EEG. Neither beat the simple, well-tuned CSP-plus-LDA approach. FBCSP actually did slightly worse, and EEGNet came in about even. My read: EEGNet just doesn't have enough training data here to show its usual advantage. This tells me feature-engineering and model architecture aren't where the next improvement is going to come from.

## Slide 10
RESULTS — MOST PROMISING FINDING
Subject Adaptation: A Little Target Data Goes a Long Way
10
Train on 8 other subjects + an increasing slice of the target subject's own data → test on that subject's separate evaluation session.
ACCURACY vs. TARGET DATA USED
Chart: % of target subject's own data used
| 0% | 5% | 10% | 20%
Mean Accuracy (%) | 50.73 | 50.77 | 54.19 | 58.3
+7.6pp
gain at 20% target data
↓ Std
14.8% → 12.0% (more consistent too)
✓ Every adaptation level improved on the 0% baseline, AND got more consistent across subjects. Subjects who generalize worst with zero target data (A05, A02) show some of the largest relative gains from adaptation. Just 20% of a subject's own data closes roughly a quarter of the gap between LOSO (~31-41%) and true single-subject performance (83%). This is the strongest lead in the whole project so far.
Notes: This is the best finding in the whole project. Instead of training purely on other people's data, I trained on 8 subjects plus a small slice of the target subject's own data, then tested on their separate session. Even 20% of that subject's own data pushes accuracy up by over 7 points — and, importantly, makes results more consistent across subjects, not just better on average. Subjects that generalize worst with zero calibration data benefit the most from a little of their own data. This points clearly at personalization as the next direction, rather than more feature engineering.

## Slide 11
RESULTS — THE REAL BOTTLENECK
It's Not the Day — It's the Person
11
Cross-session: train and test on the SAME subject, different day. Cross-subject: train on OTHER subjects, test on someone new.
Chart: Accuracy (%)
| Single-subject (same session) | Cross-session (same subject, diff. day) | Cross-subject LOSO (different subject)
Accuracy (%) | 83 | 56.75 | 38.31
✓ Cross-session (56.75%) sits far closer to single-subject (83%) than to cross-subject LOSO (38.31%). Day-to-day variability within one person is real but modest — the dominant obstacle is variability between different people's brains and electrode placement, not time. This directly supports subject adaptation as the right next direction.
Notes: This slide is the clearest way I can show why subject adaptation matters. If I train and test on the same person, just on a different day, accuracy is 56.75% — a real drop from 83%, but nowhere near as bad as training on other people entirely, which caps out around 38%. That gap tells us plainly: the hard part of this problem is who the data comes from, not when it was recorded. That's exactly why the subject-adaptation result on the previous slide is the most promising direction going forward.

## Slide 12
WRAPPING UP
Progress Summary & Next Steps
12
COMPLETED
Single-subject pipeline (83% accuracy)
Found, root-caused & fixed a data-labeling bug
Multi-subject LOSO + full optimization sweep
Filter-Bank CSP & EEGNet deep-learning baseline
Subject adaptation experiment (strongest lead)
Cross-session evaluation across all 9 subjects
Prediction-to-command mapping prototyped
NEXT STEPS
Go deeper on subject adaptation — the clearest lead
Separate cross-session vs. cross-subject adaptation cleanly
Try combining the 0-3s window with subject adaptation
Investigate why A02/A05 underperform almost everywhere
Extend the command-mapping demo toward real-time control
Revisit EEGNet if more training data becomes available
Thank you — happy to go deeper into any result.
Notes: To summarize: the pipeline now spans single-subject, multi-subject LOSO, a full optimization sweep, two alternative methods, subject adaptation, and cross-session evaluation — plus I caught and fixed a real data bug along the way. The clearest direction forward is subject adaptation: it's the one lever that consistently helped, and helped the hardest subjects the most. That's where I want to focus next, alongside extending the command-mapping prototype toward something closer to real-time control. Thank you — happy to answer questions.